Industrial Hygiene Monitoring with a Portable GC

J.N. Driscoll, HNU Systems, Inc. 160 Charlemont St., Newton, 02461

INTRODUCTION

During the seventies and eighties, considerable effort was focused on worker protection in industrial environments such as chemical plants (vinyl chloride, benzene), hospitals (ethylene oxide), and particularly hazardous waste sites. In fact, EPA's Superfund program was one of the largest industrial hygiene monitoring programs of its kind in the world. This effort continued in the nineties (1,3,butadiene, methylene chloride) and increased emphasis was placed on indoor air pollution as a result of problems, alergies and skin irritations suffered by many office workers and or students in Universities. In some cases, buildings such as the Registry of Motor Vehicles in Boston were abandoned due to the high level of complaints and sickness suffered by employees. The problem was eventually traced to improper design of the ventillation system. This sick building syndrome was also a problem for EPA in Washington DC several years ago. Thus indoor air pollution problems are becoming a significant problem for industrial hygienists.

The ability to measure low levels (ppt - ppb) is a must if indoor air pollution studies are to lead to results because the measurement of high ppb to ppm levels is insufficient. Since ppt levels are generally below the detection limit of most GC's, a concentration technique is necessary. Solid sorbents such as tenax or graphitized carbon which can be thermally cycled  are more popular for indoor air pollution studies since the entire sample is injected into the GC to improve the sensitivity.

Common Solvents found in Indoor Air Pollution

MEK

benzene

toluene

styrene

Xylenes

methylene chloride

vinyl chloride

During the ninteen seventies, the National Institute of Occupational Safety & Health (NIOSH) and Occupational Safety and Health Administration (OSHA) initiated the use of direct reading instruments in the field for industrial hygiene survey  work with subsequent collection of grab samples (charcoal or tenax tubes) to be returned to the laboratory for confirmation. This approach allows decisions to be made quickly in real time while maintaining the backup necessary for confirmation. It also allowed the "hot" spots to be determined which would have been very difficult to identify with a grab sampling technique. Although the use of portable GC's in the field by NIOSH or OSHA is not particularly widespread, more sensitive techniques may be needed for these applications. Methodology such as portable GC is necessary to meet the more stringent requirements in this field. Portable GC's with PID's or ECD's can detect ppb levels of particular contaminants without any preconcentration.

Gas Chromatography

Gas chromatography (GC) is a method of continuous chemical separation of one or more individual compounds between two phases, the stationary phase and the mobile phase (carrier gas). The components enter the stationary phase simultaneously at the injector but are eluted at different rates. The less volatile the compound (higher boiling point), the longer the compound will remain in the stationary phase. The amount of time that each compound remains in the stationary phase depends on two factors: the vapor pressure of the compound and its solubility in the stationary phase. These compounds are then detected at the end of the column with an appropriate GC detector. A plot of the output of the detector response versus time is termed a chromatogram.

Elution times may be reduced by increasing the temperature of the GC oven.  GC’s can be run isothermally (constant temperature) to separate a narrow boiling range of solutes. If the separation of low and high boiling compounds is required, temperature programming (linear increase of column temperature) is necessary.

The Retention time is defined as the time measured from the start of injection to the peak maximum and can be used to identify resolved components in mixtures. The retention time is characteristic for a compound and the stationary phase at a given temperature and is used for identification when the mixture of compounds is completely resolved. To confirm that a particular component is present requires the identification on two columns with different polarities of stationary phases. Some environmental methods allow confirmation of compound identity by comparing both retention times and detector response factors with known standards. Instruments that are configured for either dual columns with a single detector, or a single column with dual detectors (PID/FID) can combine analysis and confirmation in a single run.

There are a large number of GC packings available. Each  of these exhibit specific retention characteristics for specific compounds. Many times, a better separation is obtained more easily by changing the liquid phase than by increasing the length of the column. A properly made capillary column of 5M in length will have about 12,000-15,000 plates effective plates, more than 100 times the resolving power of a short packed column.

Porapack separations

List of GC Applications and Column Phases

| Applications | Column Phases |
| --- | --- |
| Alcohols | Carbowax 20M, OV1701 |
| Aldehydes | Carbowax 20M, OV1, SE30 |
| Amines | OV54 |
| Aromatic HC | Carbowax 20M |
| Dioxins | OV54 |
| Glycols | Carbowax 20M, OV1701 |
| Halogenated HC | OV54, OV1701 |
| Ketones | OV1, OV54 |
| PAH's | OV54, OV1701 |
| PCB's | OV54, OV1701 |
| Pesticides Triazine herbicides EPA 608 | OV351, OV225 OV54, OV1701 |
| Phenols Free Acetylated | OV1, OV225 OV54, OV1701 |
| Solvents | OV54, OV1701 |

The process of photoionization is initiated by the absorption of a photon of ultraviolet radiation energetic enough to ionize a molecule (RH) by the process shown below:

RH + h   RH+ + e-

where h  represents a photon with an energy = the ionization potential of species RH. The ions are collected in an ionization chamber which is adjacent to the lamp and contains an accelerating electrode (biased positively) and a collection electrode where the current is measured. After amplification, the current measured is proportional to concentration. The response measured will be a summation of the hydrocarbons ionized. Typical lamp energies are 10.2 eV and 11.7 eV. With the latter lamp, a PID can be used to detect aromatic hydrocarbons, alkenes, alkanes higher than butane, ketones, and unsaturated chlorinated hydrocarbons. The 11.7 lamp in a PID will allow the detection of alkanes down to methane and saturated chlorinated hydrocarbons.

Summary of GC Detector Characteristics

| Type | Response | Carrier Gas | Range |
| --- | --- | --- | --- |
| PID | organic, inorganic | Nitrogen*, helium*, hydrogen* | 2 ppb to low % |
| FID | Organic | Nitrogen*, helium*, hydrogen* | 100 ppb to % |
| FUV | Organic, inorganic, fixed | Nitrogen*, helium*, hydrogen | 0.1 ppm to low % |
| ECD | Halogenated, nitro cpds. | Argon-methane*, helium, nitrogen* | 0.1 ppb to 1 ppm |
| TCD | Organic, inorganic, fixed | Helium, hydrogen | 200 ppm to 100% |
| FPD | sulfur, phosphorus | Nitrogen*, helium*, hydrogen | 25 ppb-100 ppm |

* high purity

Specific Hydrocarbons- Gas chromatography is a very powerful  technique for separation, detection, and measurement of complex mixtures. A sample is injected onto a column that contains a stationary (solid or liquid) phase. A mobile phase (carrier gas) and controlled temperature is used to elute the sample from the column. The sample is partitioned between the gas phase and the liquid phase/solid adsorbent and moves through the column depending upon its solubility and the selectivity of the active support. If there are sufficient theoretical plates in the column, and if the selectivity is properly chosen, the sample will be separated into individual components which can be measured by a detector at the end of the column. The detector could be a photoionization detector for organics at ppb levels (11), electron capture detector for chlorinated hydrocarbons and pesticides at ppb levels, a flame ionization detector for organics at low or sub ppm levels, etc., or a far UV detector (12) for low levels of organics and inorganics.   A portable GC with two detectors is shown in Fig. 3.

DISCUSSION

Indoor Air Quality Monitoring

Generally, before an industrial hygiene audit is started, it is necessary to have advance knowlege of the solvents used (TLV's or MAC's), problems that personnel in the effected area are experiencing, a sampling strategy and an idea of exposure controls.  The goals of the program typically involve protection of workers, continuous quality control to ensure that workers are not overexposed and documentation to inform government regulators or appropriate corporate officials.

A direct reading instrument is the first place to start in a survey. The advantage of a direct reading instrument, for example, a total hydrocarbon analyzer such as a PI101, see Fig.1, is that it is possible to accomplish the following during a preliminary screening program:

*  providing an instantaneous readout of total hydrocarbon concentration in a working  environment

* measuring the total concentration profiles in a selected area in conjunction with sorbent tubes  (OSHA  survey)

* identification of contamination sources

* monitoring intake air on a continous basis

The PID will respond to a number of organics and some inorganic compounds. A list of ionization potentials (IP) is given in Table I. The PID will respond to compounds with IP's about 0.3- 0.5 eV beyond the lamp energy. The smaller the molecule, the tighter the electrons are bound and the higher the ionization potential. The larger the molecule and the more double bonds, the lower the IP. As the lamp energy is decreased, the detector will respond to fewer compounds and thus the selectivity will increase. Note that the main application for indoor air pollution studies with the 11.7 eV lamp is the detection of low molecular weight chloroalkanes  (1,1,1 tri chloroethane, trichlorofluoro methane etc.) and formaldehyde.

A second level of investigation could involve analysis with more sophisticated instrumentation (i.e., portable GC shown in Fig. ) to provide on-site detection at low (ppb) levels and identification, as far as possible, of specific components present. Although one can establish the identity of the compound(s) and relative concentrations in the field  by  collection on a solid sorbent and sending samples to a laboratory for detailed analysis, it is possible to perform this analysis in the field with a portable chromatograph such as the model 311 shown in Fig. 3.  This instrument can be programmed to automatically inject a sample of air from a contaminated area  into the GC.  A typical chromatogram (PID detector with a 10.2 eV lamp) at ppb levels is shown in Fig. 5.  The ACGIH is presently considering a reduction in the TLV of benzene from its present value of 1ppm to a new value of 0.1 ppm. Note that the GC311 still has sufficient sensitivity to measure at or below the new TLV since the detection limit is 3 ppb. If the sample is collected on a charcoal tube, the tube can be desorbed with a solvent in the field and the analysis done on-site.  This GC can be a dual detector instrument with a selection of PID, ECD or  far uv absorbance detector.

The portable GC also has the capability of using an electron capture detector (ECD) which will respond to ppb levels of chlorinated hydrocarbons which are common solvents. a typical chromatogram is shown in Fig. 6. The ECD will also respond to most freons while the PID will respond only to a few selcet freons. The ECD will also respond to many of the new freon substitutes which are typically perfluorinated species. sensitivities are expected to be excellent. The 20 most common species found in buildings are shown in Table II. most of these species can be detected by the PID with the exception of a few chlorinated species which only respond to the ECD. The ECD can also be used to determine the ventillation rates in rooms using SF6. This compound can be detected down to 0.1 ppb (see Fig. 7). By adding a known concentration of an inert gas such as SF6 to the room and  monitoring the decay of concentration with time, via:

C = C0 e -vt

where  C =  concentration

C0=initial concentration

v = ventillation rate

t = time

,  the ventillation rate can be easily determined.

Some indoor sources of VOC's are shown in Table III. Note that formaldehyde as well as long chain aliphatic hydrocarbons are also common pollutants. Formaldehyde became an important indoor air pollutant in the seventies and eighties as a result improper installation of urea-formaldehyde which that produced levels of formaldehyde which were irritationg. In the early eighties, reports of its carcinogenic nature, caused additional concern and its ultimate ban for this purpose. a gas chromatograph with a PID (11.7 eV lamp) can be used to detect ppb levels of this compound as shown in Fig. 8.

In some situations, a need exists to detect lower levels (sub ppb) in order to confirm the existance or source of a particular irritant. A GC311 was modified to include a concentrator/thermal desorber at the GC inlet. The modifications were described in detail in a previous publication (13). These modifications allowed the reproducible detection of ppt levels of aromatic hydrocarbons with a concentration factor of  >100. Atypical chromatogram for aromatic hydrocarbons at ppt levels is shown in Fig. 9.

CONCLUSIONS

The use of direct reading instruments in the field is convient and allows the industrial hygienist to confront and solve problems concerning worker safety in real time. The photoionization detectors, toxic gas analyzers and portable GC's provide a useful supplement for laboratory tests, help obtain better quality data,  ensure proper worker protection, and help solve difficult problems more quickly.

Instruments such as portable GC's enable laboratory results to be obtained in the field (even identification of specific compounds) eliminating time consuming delays and reducing the costs of the tests (14).

REFERENCES

1. Driscoll, J. N., ETO Monitoring

2. Driscoll, J.N., Amer. Lab. May 1993

3. Samet, J.M., and J.D. Spengler, Indoor Air Pollution, John Hopkins University Press, (Baltimore, MD) 1991

4. Wallace, L.A., in Indoor Air Pollution pp252

5. Pellizzari, E.D., et. al., Chemical characterization and Personal Exposure,

6. Mc Clenny

7. TO14 Method

8. Shelton 88

9.

10. Janata, J., Principles of Chemical Sensors, Plenum Press, N.Y. (1990)

11. Driscoll, J.N., and M. Duffy, "Photoionization Detector: A Versitile Tool for Environmental Analysis," Chromotography Forum, 2 (#4), May 1987

13. in press

12.  Driscoll, J.N., M. Duffy & S. Pappas, "Capillary GC Analysis

with the Far UV Absorbance Detector," Journal of Chromatography, 441, 63 (1988)

14. EPA report

List of Figures

Fig. 2  Photo of  Portable Gas Chromotograph

Fig. 3

Fig. 4 Hydrocarbon Levels in indoor Air

Fig. 5 Chromatogram of Solvents at low levels  Bz to Naph. (PID)

Fig. 6 Chromatograms of chlorinated  solvents (ECD)

Fig. 7 Chromatograms of SF6 at ppt levels

Fig. 8 Chromatogram of ppb Levels of formaldehyde

Fig. 9 GC 311 Chromatograms  ppt Levels of Aromatics with PID Detection

Fig. 10